Electric Circuits

Current:

Current:

(  Current flows because a potential difference across a conductor creates an electric field which exerts a force on free electrons in the circuit.

Conventional current: the “hypothetical” flow of positive charge (it is really electrons flowing in opposite direction)

Electromotive force or emf: the maximum difference in electrical potential between the terminals of a battery

Ohm’s Law:

Ohm’s law:

Ohm’s law is more commonly stated as:

Resistance and Resistivity:

Resistance of a wire is given by:

Resistivity depends upon temperature:

Power:

Power: 	    		applies to any circuit element

applies only to resistors

## Resistors in series: 				       Resistors in parallel:

Current is the same through each resistor	        Voltage is the same across each resistor

Voltage is split among individual resistors	        Current is split among the individual resistors