Electric Forces and Fields

mp = 1.673 ( 10-27 kg		mn = 1.675 ( 10-27 kg		me = 9.11 ( 10-31 kg

charge on a proton: 	  qp = +e = 1.602 ( 10-19 C

charge on an electron:   qe = -e = -1.602 ( 10-19 C

charge is quantized:   q = + ne    n = 0, 1, 2, …

Charged Objects:

Law of Conservation of Electric Charge: during any process, the net electrical charge of an isolated system remains constant

(  like charges repel and unlike charges attract each other

(  there are three ways to charge an object: charging by friction, charging by induction, and charging by contact

Coulomb’s Law:

(  the direction of the force is along a line connecting the two charges

(  if there are more than two charges, the net force on a charge is the vector sum of all the forces on the charge

The Electric Field:

(  the electric field is defined as:  where q0 is a small test charge

(  the force on a charge in an electric field is given by:

(  the electric field from a point charge is given by:

points away from a positive charge

points toward a negative charge