Kinematics in One Dimension

Displacement:

Average velocity: 			Instantaneous velocity:

Average acceleration: 		Instantaneous acceleration:

( An object speeds up if the velocity and acceleration point in the same direction;

it slows down if the velocity and acceleration point in opposite directions

Equations of Constant Acceleration:

freefall: gravity is the only force acting on an object (no air resistance)

Equations of Freefall:

Notes for Freefall:

( a = 9.8 m/s2 downward or a = –9.8 m/s2 if up is defined as +

( v = 0 m/s at the highest point

( freefall motion is symmetric