Magnetic Forces and Magnetic Fields

Magnetic Fields:

(  all magnets have both a north pole and a south pole

(  like poles repel, opposite poles attract

(  a magnetic field surrounds every magnet or moving electric charge (magnetic field points from north to south pole)

## Force on a Charge Moving in a Magnetic Field:

(  magnitude is given by

(  direction is given by RHR1: point fingers of right hand along  and thumb along ; your

palm points in the direction of  on a positive charge

(  a charge moving in a magnetic field will travel in a circular path of radius:

Current Carrying Wire:

(  the force on a current carrying wire in a magnetic field is give by:

(  the magnetic field a distance r away from a long-straight wire is given by:

direction is given by RHR2: point thumb in the direction of conventional current;

your fingers curl in the direction of the magnetic field

Loop of  Wire:

(  the magnetic field at the center of a circular loop of wire is given by:

(  the direction of the magnetic field inside a coil or loop of wire is given by RHR3

RHR3: curl the fingers of your right hand in the direction of conventional current; your

thumb points in the direction of  (within the loop)